OPERATOR’S

MANUAL

HEAVY DUTY

FLAIL MOWER

CAUTION: Read Manual Thoroughly Before Operation

CONTENTS

CONTENTS …………………………………………………………………………1

SAFETY  INSTRUCTIONS……………………………………………………..… 2

SAFETY  TRAINING………………………...………...………………………..….5

ASSEMBLY  INSTRUCTIONS……………………...…………………………...13

SIZING PTO SHAFT………………………………….……………………….….17

OPERATION  INSTRUCTION…………………….……………………………..18

SERVICE AND MAINTENANCE………………….…………………………….20

PARTS LIST……………………………….………………………………………24

VICTORY Implement Warranty…………………………………...……………29

SAFETY INSTRUCTIONS

|  | Before operating the Flail mower read the following safety instructions. Failure to comply with these warnings may result in serious injury or death. |
| --- | --- |

READ AND FOLLOW THE READ AND FOLLOW THE ESPECIALLY IN THE SAFETY SECTION. FAILURE TO DO SO CAN RESULT IN SERIOUS INJURY OR DEATH.

SIGNAL WORDS: The signal words DANGER, WARNING and CAUTION are used with the safety messages in this manual and with each safety sign. They are defined as follows:

DANGER: Indicates an immediate hazardous situation that, if not avoided, could result in serious injury or death. This signal word is to be limited to the most extreme situations typically for machine components that, for functional purposes, cannot be guarded.

WARNING: Indicates a potentially hazardous situation that, if not avoided, could result in serious injury or death, and includes hazards that are exposed when guards are removed. It may also be used to alert against unsafe practices.

CAUTION: Indicates a potentially hazardous situation that, if not avoided, may result in minor or moderate injury.  It may also be used to alert against unsafe practice.

EQUIPMENT SAFETY GUIDELINES

- Safety of the operator and bystanders is one of the main concerns in designing and developing a mower. However, every year accidents occur which could have been avoided by a few seconds of thought and a more careful approach to handling equipment. You, the operator, can avoid many accidents by observing the following precautions and insist those working with you, or for you, follow them.

- In order to provide a better view, certain photographs or illustrations in this manual may show an assembly with a safety shield removed. However, equipment should never be operated in this condition. Keep all shields in place. If shield removal becomes necessary for repairs, replace the shield prior to use.

- Replace any safety sign that is not readable or missing. Location of such safety signs are indicated in this manual.

SAFETY INSTRUCTIONS

- Never use alcoholic beverages or drugs that can hinder alertness or coordination while operating this equipment. Consult your doctor about operating this machine while taking prescription medications.

- Under no circumstances should children under the age of 18 be allowed to work with this equipment. Do not allow persons to operate or assemble this unit until they have read this manual and have developed a thorough understanding of the safety precautions and how it works. Review the safety instructions with all users annually.

- This equipment is dangerous to children and persons unfamiliar with its operation. The operator should be a responsible, properly trained and physically able person familiar with farm machinery and trained in this equipment’s operations. If the elderly are assisting with farm work, their physical limitations need to be recognized and accommodated.

- Use a tractor equipped with a Roll Over Protective System and seat belts. (ROPS)

- Never exceed the limits of a piece of machinery. If its ability to do a job, or to do so safely, is in question-DON’T TRY IT.

- Do not modify the equipment in any way. Unauthorized modification could result in serious injury or death and may impair the function and life of the equipment.

- In addition to the design and the confirmation of this implement, including safety signs and safety equipment, hazard control and accident prevention are dependent upon the awareness, concern, prudence, and proper training of personnel involved in the operation, transport, maintenance, and storage of the machine. Refer also to safety messages and operation instruction in each of the appropriate sections of the tractor and mower manuals. Pay close attention to the safety signs affixed to the tractor and the mower.

SAFETY TRAINING

- Safety is a primary concern in the design and manufacturing of our product. Unfortunately, our efforts to provide safe equipment can be wiped out by a single careless act of an operator or bystander.

- In addition to the design and configuration of equipment, hazard control and accident prevention are dependent upon the awareness, concern, prudence and proper training of personnel involved in the operation, transport, maintenance and storage of this equipment.

- It has been said, “The best safety device is an informed, careful operator.”  We ask you to be that kind of operator.  It is the operator’s responsibility to read and understand all safety and operating instructions in the manual and to follow them. Accidents can be avoided.

- Working with unfamiliar equipment can lead to careless injuries. Read this manual, and the manual for your tractor, before assembly or operating, to acquaint yourself with the machines. If this machine is used by any person other than you, or is loaned or rented, it is the Flail mower owner’s responsibility to make certain that the owner's manual be available to the operator prior to operating:

1-Reads and understands the operator’s manuals.

2-Is instructed in safe and proper use.

- Know your controls and how to stop the tractor, engine, and mower quickly in an emergency.  Read this manual and the one provided with your tractor.

- Train all new personnel and review instructions frequently with existing workers. Be certain only a properly trained and physically able person will operate the machinery. A person who has not read and understood all operating and safety instructions is not qualified to operate the machine. An untrained operator exposes himself and bystanders to possible serious injury or death. If the elderly are assisting with farm work, their physical limitations need to be recognized and accommodated.

SAFETY TRAINING

PREPARATION

- Never operate the tractor and mower until you have read and completely understand this manual, the Tractor Operator’s Manual, and each of the safety messages found on the safety signs on the tractor and mower.

- Personal protection equipment including hardhat, safety glasses, safety shoes, and gloves are recommended during assembly, installation, operation, adjustment, maintenance, repairing, removal, or moving the implement. Do not allow long hair, loose fitting clothing, or jewelry to be around equipment.

- PROLONGED EXPOSURE TO LOUD NOISE MAY CAUSE PERMANENT HEARING LOSS! Tractors with or without mowers attached can often be noisy enough to cause permanent, partial hearing loss. We recommend that you wear hearing protection on a full-time basis if the noise in the operator’s position exceeds 80 db.  Noise over 80 db on a long-term basis can cause severe hearing loss. Noise over 90 db adjacent to the opera-tor over a long-term basis may cause permanent, total hearing loss. NOTE: Hearing loss from loud noise (from tractors, chain saws, radios, and other such sources close to the ear) is cumulative over a lifetime without hope of natural recovery.

- Operate the mower only with a tractor equipped with an approved Roll-Over-Protective System (ROPS). Always wear your seat belt. Serious injury or even death could result from falling off the tractor — particularly during a turnover when the operator could be pinned under the ROPS or the tractor.

- Clear area to be worked of stones, branches or other debris that might be thrown or entangled in the mower, causing injury or damage.

- Operate only in daylight or good artificial light.

- Ensure mower is properly mounted, adjusted and in good operating condition.

- Ensure that all safety shielding and safety signs are properly installed and in good condition.

SAFETY TRAINING

- Do not operate unless all personnel, livestock, and pets are several hundred feet away to prevent injury by thrown objects.

- Never operate tractor and Flail mower under trees with low hanging limbs. Operators can be knocked off the tractor and then run over by the rotating tines.

- The rotating parts of this machine have been designed and tested for rugged use. However, they could fail upon impact with heavy, solid objects such as steel guardrails and concrete abutment. Such impact could cause the broken objects to be thrown outward at very high velocities. To reduce the possibility of property damage, serious injury, or even death, never allow the working tines to contact such obstacles.

- Stop Flail mower and tractor immediately upon striking an obstruction.  Turn engine off, remove key, inspect and repair any damage before resuming operation.

- Stay alert for uneven terrain, holes, rocks, and roots and other hidden hazards. Keep away from drop-offs and hazards that could cause roll over. Use extreme care and maintain minimum ground speed when trans-porting or operating on hillsides, over rough ground and when operating close to ditches or fences. Be careful and slow down when turning sharp corners and changing direction on slopes. Do not start or stop suddenly on slopes. Avoid operation on steep slopes. In extremely uneven terrain, rear wheels weights, front tractor weight, and/or tire ballast should be used to improve stability.

- Pass Flail mower diagonally through sharp dips and avoid sharp drops to prevent “hanging up” tractor and Flail mower.  Practice will improve your skills in maneuvering on rough terrain. Always cut down slopes, never across the face. Always check tractor manual for proper use on slopes.

SAFETY TRAINING

MAINTENANCE SAFETY

- Good maintenance is your responsibility.  Poor maintenance is an invitation to trouble.

    - Follow good shop practices.

    - Keep service area clean and dry

    - Be sure electrical outlets and tools are properly grounded

    - Use adequate light for the job at hand.

- Make sure there is plenty ventilation. Never operate the engine of the towing vehicle in a closed building. The exhaust fumes may cause asphyxiation.

- Before working on this machine, disengage the PTO, shut off the engine, set the brakes, and remove the ignition keys.

- Be certain all moving parts on attachments have come to a complete stop before attempting to perform maintenance.

- Never work under equipment unless it is blocked securely.

- Always use personal protection devices such as eye, hand and hearing protectors, when performing any service or maintenance.

- Frequently check mower tines. They should be sharp, free of nicks and cracks and securely fastened.

- Periodically tighten all bolts, nuts, and screws and check that all cotter pins are properly installed to ensure unit is in safe condition.

- When completing a maintenance or service function, make sure all safety shields and devices are installed before placing unit in service.

- After servicing, be sure all tools, parts and service equipment are removed from mower.

- Do not allow debris, grease or oil to build up on any deck or platform.

- Where replacement parts are necessary for periodic maintenance and servicing, genuine factory replacement parts must be used to restore your equipment to original

SAFETY TRAINING

specifications.

- The manufacturer will not be responsible for injuries or damages caused by use of unapproved parts and/or accessories.

- A fire extinguisher and the first aid kit should be kept readily accessible while performing maintenance on this equipment.

STORAGE SAFETY

- Following operation, or when unhooking the mower, stop the tractor, set the brakes, disengage the PTO, shut off the engine and remove the ignition keys.

- Store the unit in an area away from human activity.

- Do not park equipment where it can be exposed to direct contact to livestock for long periods of time. Damage and livestock injury could result.

- Make sure all parked machines are on a hard, level surface and engage all safety devices.

ASSEMBLY INSTRUCTIONS

- Take our mower and all the parts from box.

- Assemble the arms on mower. Assemble the bolt on the hole. All the BCRI were fully assembled when tested it in factory, so you can assemble it. Because it is really heavy, so it will take you hours to assemble it, just be patient.

ASSEMBLY INSTRUCTIONS

- Assemble the 3 point hitch on mower, then connect hydraulic oil pipe to tractor.

- Use a stick to test if oil in the transmission every month. Factory already fulfill 1L SAE 85W/90 gear oil into the transmission,  please use a stick to test if enough oil in it every month. The transmission can load 2L oil, it need to fulfill 1L gear oil at least.

ASSEMBLY INSTRUCTIONS

- Check the belt tension every month.

- Adjust the mower height and roller height if you want to adjust grass cutting height.

ASSEMBLY INSTRUCTIONS

- Grease all the nipple.

SIZING PTO SHFAT

STEP 1   Cutting the PTO shaft to length.

NOTE: Be sure to cut equal lengths of each PTO shaft section. Clamp end of PTO shaft in a vice and cut off shield where marked. (Figure 1-A & 1-B)                                  Figure 1-A

STEP 2   Using cut section of the shield as a guide cut shaft off the same amount. (Figure 2)

F

Figure 1-B

STEP 3   Repeat steps 1 and 2 for other PTO shaft

section.

STEP 4   Use a file to deburr PTO shafts. Clean up all chips, burrs and filings from both ends of the PTO shaft.

Figure 2

OPERATING INSTRUCTIONS

WARNING: IF MOWER IS RAISED UP SO THAT PTO SHAFT IS AT AN ANGLE SHARPER THAN 35 DEGREES PTO MUST BE STOPPED!

STEP 1   Before each use perform the maintenance described in maintenance section.

STEP 2    Read, understand, and follow the information on safety training, preparation, starting and stopping safety, operational safety, transport safety warning sections of this manual.

STEP 3    With the Flail mower positioned on level ground, adjust the tractor lift arms so that when lifted, the rotor bar remains parallel to the ground.

STEP 4    With the Flail mower attached to the tractor, raise and support the mower with suitable blocks.  Adjust the skids, located on the sides of the mower.  The adjustment bolts for both right and left sides should be positioned in the same adjustment hole. This allows the mower to mow the same depth on each side.

Note: Never attempt to adjust the Flail mower while the tractor is running.

STEP 5    Raise the mower and remove the blocks. Lower the mower to the ground.

STEP 6    With the tractor at idle RPM and the mower lifted off of the ground, engage PTO and slowly advance throttle to 540 PTO RPM. NOTE: Flail mower is designed to run at

540 PTO RPM only.

STEP 7    Select a low gear for the tractor and begin to move forward. Tractor ground speed is to be controlled by gear selection only and not engine speed. As the tractor moves forward, slowly lower the mower down. Allow the mower tines to gradually engage the ground.

NOTE: Do not allow the tractor engine or Flail mower to bog down or stall. This causes undue wear and tear on the mower and tractor.  If this continues to happen reduce ground speed and raise working depth of Flail mower.  Never attempt to re-move objects from the rotor bar until the tractor has been shut down and the mower tines have completely stopped.

OPERATING INSTRUCTIONS

Never travel at a fast ground speed while using the mower, this could damage it. Never attempt to turn the tractor or travel in reverse with the PTO engaged and the mower in the ground. Always raise the mower out of the ground when backing up or attempting to turn. Failure to due so may cause damage to the mower.

STEP 8   After each use clean all debris from the mower tines. Replace any missing or illegible safety decals. Inspect for any damaged or worn parts and replace before next use.  Store Flail mower in a dry environment.

SERVICE AND MAINTENANCE

3.1 Service

3.1.1   FLUIDS AND LUBRICANTS

1. Grease:

Use only a grade Type II tube grease.

2. Storing Lubricants:

Your machine can operate at top efficiency only if clean lubricants are used. Use clean containers to handle all lubricants. Store them in an area protected from dust, moisture and other contaminants.

3.1.2	GREASING

1.	Use a hand-held grease gun for all greasing.

2.	Wipe grease nipple with a clean cloth before greasing, to avoid injecting dirt and grit.

3.	Replace and repair broken nipples immediately.

4.	If nipples will not take grease, remove and clean thoroughly. Also clean lubricant passageway. Replace nipple if necessary.

3.2 Maintenance

The recommended period is based on normal operating conditions. Severe or unusual conditions may require more frequent maintenance.

3.2.1 8 Hours or Daily Maintenance

- Check all nuts and bolts in connection parts, replace if required.

Pump grease into each grease nipple three to five times.

Clean the implement; take away all debris and residue.4.

3.2.2 Season Maintenance

1. Check the machine as above for daily maintenance.

2. Check the bearings of blade spindles for wear and tear. If warn, disassemble, clean and replace them if it is necessary, grease as required.

3. Check the drive belt if tighten.

SERVICE AND MAINTENANCE

3.2.3 Annual Maintenance

- Thoroughly clean the flail mower of debris and residue.

- Drain the gearbox and clean it thoroughly.  Fill with new gear oil up to the dedicated oil level.

- Check and clean blade axles. Check oil seals and replace if necessary.

- Check all blades, replace them if they are warn out or damaged.

- Repair the side skirts; return them to original technical condition. Replace damaged or broken	 protective devices.

- Remove the drive shaft from the machine. Pull the PTO shaft apart. Check and replace any.	 components that are damaged or worn. Install the PTO shaft on the machine. The PTO shaft should telescope easily and the guard turn freely on the shaft, grease if necessary.

|  | 8hrs/Daily | 40hrs/Weekly | Annually |
| --- | --- | --- | --- |
| Lubricate PTO Shaft | Yes | Yes | Yes |
| Lubricate Caster Wheels | Yes | Yes | Yes |
| Lubricate Blade Spindle | Yes | Yes | Yes |
| Clean Machine |  |  | Yes |
| Lubricate and clean PTO Shaft Cover |  |  | Yes |

3.2.4 PTO SHAFT MAINTENANCE

The PTO shaft is designed to telescope to allow for dimensional changes as the machine goes through its operating range. A tubular guard encloses the driving components and is designed to remain stationary on a turning shaft when required. The shaft should telescope easily and the guard turn freely on the shaft at all times. Annual disassembly, cleaning and lubrication is recommended to insure that all components function as intended. To maintain the shaft, follow this procedure:

- Remove the shaft from the machine.

- Pull shaft apart.

- Use a screwdriver to pry the tabs out of the sleeves on each end. There are 3 tabs per guard.

- Pull the shaft out of the plastic tubular guard.

- Use a solvent to clean the male and female portions of the telescoping ends.

- Apply a light coat of grease to each end.

- Clean grooves on each end where the tabs are located. Clean each tab also.

- Apply a light coat of grease to each groove.

- Insert the shaft into its respective guard and align the slots with the groove.

- Insert the tabs through the slots and seat in the groove.

- Check that each guard turns freely on the shaft.

SERVICE AND MAINTENANCE

- Assemble the shaft.

- Check that the shaft telescopes easily.

- Replace any components that are damaged or worn.

- Install the shaft on the machine.

3.2.5 GEARBOX AND HYDRAULIC MAINTENANCE

Maintain the gearbox and hydraulic components by following this procedure:

- Check if the belt is wear out, or replace a new belt.

- Check if the tooth of gear is wear out, or replace a new gear.

- Dirt, debris and salt has to be washed away immediately after using the mower in such circumstances.

3.3 STORAGE

After the season’s use, the machine should be thoroughly inspected and prepared for storage. Repair or replace any worn or damaged components to prevent any unnecessary down time at the start of next season. To insure a long, trouble free life, follow the procedure outlined below:

- Thoroughly wash the machine using a pressure washer to remove all dirt, mud, debris and residue.

- Inspect the blades and rotor for damage or entangled material. Repair or replace damaged parts. Remove all entangled material.

- Lubricate all grease nipples. Make sure that all grease cavities have been filled with grease to	 remove any water residue from the inside.

- Touch up all paint nicks and scratches to prevent rusting.

- Move to storage area.

- Select an area that is dry, level and free of debris.

- Unhook from tractor.

- If the machine cannot be placed inside, cover with a waterproof tarpaulin and tie securely in place.

Store the machine in an area away from human activity. Do not allow children to play on or around the stored machine.

SERVICE AND MAINTENANCE

3.4 Trouble Shooting

The Flail mower is designed to work on unplowed and plowed field. It is a simple and reliable system that requires minimal maintenance.

In the following section, we have listed many of the problems, causes and solutions to the problems that you may encounter.

| Problem | Possible Cause | Solution |
| --- | --- | --- |
| PTO Shaft inclined too much | Flail mower failed horizontal level | Adjust the horizontal level of the Mower |
|  | One side sway chain of tractor is too short | Adjust the chain |
| PTO Shaft injured | Direction mistaken | Re-assemble correctly |
|  | Grease deficient | Rinse needle and pump grease sufficiently |
|  | Angle of PTO Shaft is too big or is gripped | Limit the rising position and re-lock the position |
|  | Flail mower fallen down the soil sharply | Fall the Mower down the soil smoothly |
| Noise in gearbox | The clearance between the two helical bevel gears is too large | Adjust this clearance |
|  | Bearing injured | Replace bearing |
|  | Tooth of gear broken | Replace gear |
| Trouble rotation of cultivator shaft | Gear or bearing injured or gripped | Replace gear or bearing |
|  | There was no clearance between the two helical bevel gears | Adjust the clearance of the helical bevel gear pair |
|  | Out of shape of left side plane | Correct side plane |
|  | Cultivator shaft crooked or out of shape | Correct or replace cultivator shaft |
|  | Cultivator shaft twined with grass or hold soil seriously | Clear away grass or soil |

PARTS LIST

PARTS LIST

| No | Part No. | Name & Specification | QTY |
| --- | --- | --- | --- |
| 1 | 02.BCRI.140.013.A | roller for BCRI140 | 1 |
|  | 02.BCRI.160.013.A | roller for BCRI160 |  |
|  | 02.BCRI.180.013.A | roller for BCRI180 |  |
|  | 02.BCRI.200.013.A | roller for BCRI200 |  |
|  | 02.BCRI.220.013.A | roller for BCRI220 |  |
| 2 | 03.08.893,1.Φ72 | circlip for hole Φ72 | 2 |
| 3 | 03.05.281.2207 | spherical ball bearing 2207 | 2 |
| 4 | 02.BCRI.00.014.A | roller bearing seat | 2 |
| 5 | 03.13.01.BCRI | Comer gear box for BCRI | 1 |
| 6 | 03.02.6184.M14 | locking nut M14,prevailing torque type all-metal hexagon nuts,style 1 | 4 |
| 7 | 03.03.97,1.Φ14 | flat washer Φ14 | 8 |
| 8 | 03.01.5783.M14x40 | full thread hexagon head bolt M14x40 | 4 |
| 9 | 03.01.5783.M10x35 | full thread hexagon head bolt M10x35 | 6 |
| 10 | 03.03.97,1.Φ10 | flat washer Φ10 | 13 |
| 11 | 02.BCRI.140.042.A | rear safety bar for BCRI140 | 1 |
|  | 02.BCRI.160.042.A | rear safety bar for BCRI160 |  |
|  | 02.BCRI.180.042.A | rear safety bar for BCRI180 |  |
|  | 02.BCRI.200.042.A | rear safety bar for BCRI200 |  |
|  | 02.BCRI.220.042.A | rear safety bar for BCRI220 |  |
| 12 | 02.BCRI.140.101.A | rear scraper for BCRI140 | 1 |
|  | 02.BCRI.160.101.A | rear scraper for BCRI160 |  |
|  | 02.BCRI.180.101.A | rear scraper for BCRI180 |  |
|  | 02.BCRI.200.101.A | rear scraper for BCRI200 |  |
|  | 02.BCRI.220.101.A | rear scraper for BCRI220 |  |
| 13 | 02.BCRI.00.135.A+ | PTO cover | 1 |
| 14 | 03.03.97,1.Φ8 | flat washer Φ8 | 8 |
| 15 | 03.04.93.Φ8 | spring washer Φ8 | 4 |
| 16 | 03.01.5783.M8x20 | full thread hexagon head bolt M8x20 | 8 |
| 17 | 03.01.5783.M12x40 | full thread hexagon head bolt M12x40 | 4 |
| 18 | 03.03.97,1.Φ12 | flat washer Φ12 | 40 |
| 19 | 03.02.6184.M12 | locking nut M12,prevailing torque type all-metal hexagon nuts,style 1 | 22 |
| 20 | 03.03.96,1.Φ12 | big flat washer Φ12 | 4 |
| 21 | 03.04.93.Φ12 | spring washer Φ12 | 7 |
| 22 | 03.01.5783.M12x30 | full thread hexagon head bolt M12x30 | 8 |
| 23 | 02.BCRI.00.016.A+ | BCRI gear box bracket | 1 |
| 24 | 02.BCRI.00.017.A+ | BCRI upper pulley cover | 1 |
| 25 | 03.02.6184.M8 | locking nut M8,prevailing torque type all-metal hexagon nuts,style 1 | 4 |
| 26 | 03.03.96,1.Φ8 | big flat washer Φ8 | 4 |
| 27 | 02.BCRI.00.018.A+ | BCRI lower pulley cover | 1 |
| 28 | 02.BCRI.00.103 | plate | 1 |
| 29 | 03.02.6182.M6 | locking nut M6, prevailing torque type hexagon nuts | 2 |
| 30 | 03.03.97,1.Φ6 | flat washer Φ6 | 4 |
| 31 | 03.01.5783.M6x20 | full thread hexagon head bolt M6x20 | 2 |
| 32 | 03.10.28701.33x80 | power lock 33x80 | 1 |
| 33 | 02.BCRI.00.123 | upper pulley | 1 |
| 34 | 03.12.BX.17x1295 | belt BX 17x1295 (51 inch) | 4 |
| 35 | 03.01.5783.M12x35 | hexagon head bolt M12x35 | 14 |
| 36 | 02.BCRI.00.015.A | BCRI foot | 2 |
| 37 | 03.01.5783.M12x80 | full thread hexagon head bolt M12x80 | 2 |
| 38 | 02.BCRI.00.021 | T plate | 1 |
| 39 | 02.BCRI.140.041.A | front safety bar for BCRI140 | 1 |
|  | 02.BCRI.160.041.A | front safety bar for BCRI160 |  |
|  | 02.BCRI.180.041.A | front safety bar for BCRI180 |  |
|  | 02.BCRI.200.041.A | front safety bar for BCRI200 |  |
|  | 02.BCRI.220.041.A | front safety bar for BCRI220 |  |
| 40 | 03.02.6184.M10 | locking nut M10,prevailing torque type all-metal hexagon nuts,style 1 | 6 |
| 41 | 02.BCRI.140.014 | shaft of BCRI140 protection plate | 1 |
|  | 02.BCRI.160.014 | shaft of BCRI160 protection plate |  |
|  | 02.BCRI.180.014 | shaft of BCRI180 protection plate |  |
|  | 02.BCRI.200.014 | shaft of BCRI200 protection plate |  |
|  | 02.BCRI.220.014 | shaft of BCRI220 protection plate |  |
| 42 | 03.07.91.4x25 | cotter pin 4x25 | 2 |
| 43 | 02.BCRI.00.136.A+ | protection plate,70mm width 180mm length |  |
|  | 02.BCRI.00.137.A+ | protection plate,50mm width 180mm length |  |
|  | 02.BCRI.00.139.A+ | protection plate,40mm width 180mm length |  |
| 44 | 02.BCRI.00.122 | BCRI lower pulley | 1 |
| 45 | 03.10.28701.40x80 | power lock 40x80 | 1 |
| 46 | 02.BCRI.00.024 | rotor shaft end left bearing | 1 |
| 47 | 03.06.13871.40x85x12 | oil seal 40x85x12 | 1 |
| 48 | 03.05.281.2308 | spherical ball bearing 2308 | 2 |
| 49 | 03.06.13871.50x90x8 | oil seal 50x90x8 | 2 |
| 50 | 03.08.893,1.Φ90 | circlip for hole Φ90 | 2 |
| 51 | 02.BCRI.140.022 | rotor shaft for BCRI140 | 1 |
|  | 02.BCRI.160.022 | rotor shaft for BCRI160 |  |
|  | 02.BCRI.180.022 | rotor shaft for BCRI180 |  |
|  | 02.BCRI.200.022 | rotor shaft for BCRI200 |  |
|  | 02.BCRI.220.022 | rotor shaft for BCRI220 |  |
| 52 | 03.02.6184.M16 | locking nut M16,prevailing torque type all-metal hexagon nuts,style 1 | 1 |
| 53 | 02.BCRI.00.001.A | 800gr forging hammer | N |
| 54 | 03.01.5782.M16x95 | hexagon head bolt M16x95 | 1 |
| 55 | 03.08.894,1.Φ40 | Φ40 circlip for shaft, type A | 1 |
| 56 | 02.BCRI.00.023 | rotor shaft end right bearing | 1 |
| 57 | 03.15.1152.M10x1 | oil nipple M10x1 | 4 |
| 58 | 03.02.812.M30 | round nut M30 | 2 |
| 59 | 03.04.93.Φ30 | spring washer Φ30 | 2 |
| 60 | 03.01.825.M16 | eyebolt M16 | 2 |
| 61 | 02.BCRI.140.011.A | BCRI140 mower body | 1 |
|  | 02.BCRI.160.011.A | BCRI160 mower body |  |
|  | 02.BCRI.180.011.A | BCRI180 mower body |  |
|  | 02.BCRI.200.011.A | BCRI200 mower body |  |
|  | 02.BCRI.220.011.A | BCRI220 mower body |  |
| 62 | 02.BCRI.00.026 | turning plate | 1 |
| 63 | 03.03.97,1.Φ30 | flat washer Φ30 | 10 |
| 64 | 02.BCRI.00.109 | pin for turning cylinder | 2 |
| 65 | 03.15.1152.M6x1 | grease nipple M6x1 | 3 |
| 66 | 02.BCRI.00.025 | turning plate base | 1 |
| 67 | 03.03.97,1.Φ24 | flat washer Φ24 | 2 |
| 68 | 02.BCRI.00.138 | long pin | 2 |
| 69 | 03.11.12613.80x85x60 | oilless bearing 80x85x60 | 2 |
| 70 | 03.03.97,1.Φ44 | flat washer Φ44 | 1 |
| 71 | 03.02.6184.M24 | locking nut M24,prevailing torque type all-metal hexagon nuts,style 1 | 2 |
| 72 | 03.02.6184.M42 | locking nut M42,prevailing torque type all-metal hexagon nuts,style 1 | 1 |
| 73 | 02.BCRI.00.130 | safety locking hitch | 1 |
| 74 | 03.07.DIN11023.Φ56 | locking pin Φ56 | 1 |
| 75 | 02.BCRI.00.019 | pin | 1 |
| 76 | 03.04.93.Φ10 | spring washer Φ10 | 1 |
| 77 | 03.01.5783.M10x20 | full thread hexagon head bolt M10x20 | 1 |
| 78 | 02.BCRI.00.037 | turning cylinder bracket | 1 |
| 79 | 03.17.3452.10x2 | O ring 10x2 | 1 |
| 80 | 02.BCRI.00.115 | pipe adapter 2 | 1 |
| 81 | 02.BCRI.00.105 | connector 1 | 1 |
| 82 | 03.18.982.Φ14 | combined washer 14 | 3 |
| 83 | 02.BCRI.00.106 | connector 2 | 2 |
| 84 | 02.BCRI.00.V01 | hydraulic safety lock | 1 |
| 85 | 03.18.982.Φ18 | combined washer Φ18 | 2 |
| 86 | 02.BCRI.00.104 | turning cylinder | 1 |
| 87 | 02.BCRI.00.020 | pin | 1 |
| 88 | 02.BCRI.00.107 | pipe adapter 1 | 1 |
| 89 | 03.18.982.Φ16 | combined washer 16 | 4 |
| 90 | 02.BCRI.00.108 | hollow bolt | 2 |
| 91 | 02.BCRI.00.116 | BCRI oil pipe 2, 2100mm Φ6.4 | 1 |
| 92 | 02.BCRI.00.V02 | BCRI hydraulic oil flow speed valve | 1 |
| 93 | 02.BCRI.00.118 | BCRI oil pipe 3, 1900mm Φ6.4 | 1 |
| 94 | 03.18.982.G1/2 | washer G1/2 | 2 |
| 95 | 03.16.5860.G1/2 | quick-change coupler G1/2 | 2 |
| 96 | 02.BCRI.00.117 | BCRI oil pipe 1, 4080mm Φ6.4 | 1 |
|  | 03.14.01.T5-1800 | common PTO shaft, T5-1800 | 1 |

PARTS LIST

| No | Part No. | Name & Specification | QTY |
| --- | --- | --- | --- |
| 1 | 02.BCRI.00.124 | rubber cover | 2 |
| 2 | 03.07.DIN11024.Φ4 | split pin Φ4 | 2 |
| 3 | 02.EF.00.116 | support foot pin | 2 |
| 4 | BP-BCRI200-36 | support foot | 1 |
| 5 | 03.07.DIN11023.Φ56 | linch pin | 3 |
| 6 | 02.BCRI.00.131 | lower hitch pin | 2 |
| 7 | 03.01.5782.M28x170 | hexagon head bolt M28x170 | 1 |
| 8 | 03.02.889,1.M28 | locking nut M28, prevailing torque type hexagon nuts, style 1 | 1 |
| 9 | 02.BCRI.00.038 | small extra hitch | 1 |
| 10 | 02.BCRI.00.028.A+ | 3 point hitch | 1 |
| 11 | 02.BCRI.00.033 | short pin | 1 |
| 12 | 03.03.97,1.Φ24 | flat washer Φ24 | 3 |
| 13 | 03.02.889,1.M24 | locking nut M24, prevailing torque type hexagon nuts, style 1 | 3 |
| 14 | 02.BCRI.00.113 | protection pin | 2 |
| 15 | 02.BCRI.00.029.A+ | hitch brackt | 1 |
| 16 | 03.11.12613.30x34x40 | oiless bearing 30x34x40 | 8 |
| 17 | 02.BCRI.00.030.A | left arm | 1 |
| 18 | 03.15.1152.M10x1 | grease nipple M10x1 | 6 |
| 19 | 02.BCRI.00.119 | BCRI oil pipe 4, 2550mm Φ6.4 | 2 |
|  | 02.BCRI.00.120 | BCRI oil pipe 5, 2400mm Φ6.4 |  |
| 20 | 03.18.982.G1/2 | washer G1/2 | 2 |
| 21 | 03.16.5860.G1/2 | quick release coupling G1/2 | 2 |
| 22 | 03.02.41.M12 | hexagon nut M12 | 1 |
| 23 | 03.04.93.Φ12 | spring washer Φ12 | 2 |
| 24 | 03.01.5783.M12x35 | full thread hexagon head bolt M12x35 | 3 |
| 25 | 03.03.97,1.Φ12 | flat washer Φ12 | 2 |
| 26 | 02.BCRI.00.032 | pin | 2 |
| 27 | 02.BCRI.00.052 | swing cylinder | 1 |
| 28 | 02.BCRI.00.031 | right arm | 1 |
| 29 | 02.BCRI.00.138 | long pin | 2 |
| 30 | 02.BCRI.00.034 | support feet | 1 |
| 31 | 03.01.5782.M8x70 | hexagon head bolt M8x70 | 1 |
| 32 | 03.04.93.Φ8 | spring washer Φ8 | 1 |
| 33 | 03.03.97,1.Φ8 | flat washer Φ8 | 1 |
| 34 | 02.BCRI.00.PC16 | Pipe Clamp | 1 |
| 35 | 02.BCRI.00.130 | upper hitch pin | 1 |
| 36 | 02.BCRI.00.112 | PTO hook | 1 |
| 37 | 02.BCRI.00.111 | spring plate | 1 |
| 38 | 03.03.97,1.Φ6 | flat washer Φ6 | 1 |
| 39 | 03.04.93.Φ6 | spring washer Φ6 | 1 |
| 40 | 03.01.5783.M6x12 | full thread hexagon head bolt M6x12 | 1 |

Victory Implement Warranty

Warranty

Victory warrants to the original purchaser that this Victory product will be free from defects in material and workmanship beginning on the date of purchase by the end user according to the following schedule when used as intended and under normal service and conditions for personal use.

Overall Unit and Driveline: One year Parts and Labor

Gearbox: One year on all components.

Blades and Belts: Considered wear items.

This Warranty is limited to the replacement of any defective part by Victory and the installation by the dealer of any such replacement part, and does not cover common wear items. Victory reserves the right to inspect any equipment or parts which are claimed to have been defective in material or workmanship.

This Warranty does not apply to any part or product which in Victory’s judgment shall have been misused or damaged by accident or lack of normal maintenance or care, or which has been repaired or altered in a way which adversely affects its performance or reliability, or which has been used for a purpose for which the product is not designed. Misuse also specifically includes failure to properly maintain oil levels, grease points, and driveline shafts.

Claims under this Warranty should be made to the dealer which originally sold the product and all warranty adjustments must be made through an authorized Victory dealer. Victory reserves the right to make changes in materials or design of the product at any time without notice.

This Warranty shall not be interpreted to render Victory liable for damages of any kind, direct, consequential, or contingent to property. Furthermore, Victory shall not be liable for damages resulting from any cause beyond its reasonable control. This Warranty does not extend to loss of crops, any expense or loss for labor, supplies, rental machinery or for any other reason.

No other warranty of any kind whatsoever, express or implied, is made with respect to this sale; and all implied warranties of merchantability and fitness for a particular purpose which exceed the obligations set forth in this written warranty are hereby disclaimed and excluded from this sale.

This Warranty is not valid unless registered with Victory within 30 days from the date of purchase by the end user.

# Text boxes

When you push it, its tension is ok if you only can push less then 2cm.

Adjust these two bolt to adjust the belt tension.

Adjust these bolts to adjust mower height.

Adjust these bolts to adjust roller height.